## Slide 1
INDENG 290 ENERGY ANALYTICS
PROJECT PRESENTATION
The Energy Implications of
AI-Driven Data Centers
Team Papago
Linzhi (Sharon) Wu · Kelly Zeng
UC Berkeley · Spring 2026 · May 2026

## Slide 2
ELEMENT 3 · FOCUS QUESTIONS
Three questions guiding the project
01
How much additional electricity demand will AI-driven data centers generate over the next 5–10 years?
Forecasting
02
How does this demand affect wholesale prices, peak load, and grid stability in regions with concentrated data-center activity?
Grid stress
03
To what extent can renewable adoption and hardware efficiency offset the environmental impact?
Trade-offs
Unchanged from the project proposal.
Papago
INDENG 290 Energy Analytics
02 / 16

## Slide 3
ELEMENT 4 · STAKEHOLDER PERSPECTIVE
Who is this for, and what decision does it inform?
PRIMARY STAKEHOLDER
State public utility commissions and grid operators
Specifically: Virginia SCC, Texas PUCT, California CPUC, and the operators of PJM, ERCOT, and CAISO.
Secondary: institutional investors evaluating utilities and hyperscaler infrastructure exposure.
DECISIONS OUR ANALYSIS AIMS TO INFORM
Capacity & transmission
Whether to approve new gas, nuclear, or transmission build to serve hyperscaler load.
Cost allocation
Whether large loads should pay a separate rate class (Virginia GS-5, Oregon's dedicated tariff).
Interconnection rules
Whether to require demand response, on-site generation, or co-located storage as a connection condition.
Reliability backstops
Whether to extend price caps, mandate flexible loads, or fast-track generation procurement.
Papago
INDENG 290 Energy Analytics
03 / 16

## Slide 4
THE PHENOMENON
U.S. data-center electricity use is on track to triple by 2030
Chart: TWh / year
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Low (LBNL) | 76 | 80 | 90 | 105 | 130 | 176 | 200 | 225 | 255 | 290 | 325 | 365 | 400
Mid (LBNL midpoint) | 76 | 80 | 90 | 105 | 130 | 176 | 215 | 255 | 300 | 350 | 410 | 470 | 525
High (IEA / Goldman) | 76 | 80 | 90 | 105 | 130 | 176 | 230 | 285 | 345 | 415 | 500 | 590 | 680
176
TWh
2023 actual
~4.4% of U.S. electricity
525
TWh
2030 LBNL midpoint projection
+165%
Goldman Sachs global growth
2023–2030
Source: Lawrence Berkeley National Lab 2024 U.S. Data Center Energy Usage Report; IEA Energy and AI (2025); Goldman Sachs Research (2025).
Papago
INDENG 290 Energy Analytics
04 / 16

## Slide 5
GEOGRAPHIC CONCENTRATION
Demand is wildly concentrated in five states
Chart: Grid power demand (GW)
| Virginia | Texas | Oregon | California | Georgia | Arizona | Ohio | Iowa
2025 | 12.1 | 9.7 | 4 | 3.4 | 3.2 | 3.2 | 2.9 | 2.7
2030 (forecast) | 22 | 18.5 | 6.5 | 4.5 | 7 | 6 | 7.5 | 4.5
THE HEADLINE
80%
of U.S. data-center load is in 15 states. Virginia alone hosts ~26% of the country's total — and ~26% of Virginia's electricity.
Implication: any analysis of grid stress must be regional. National averages mask the failure modes.
Source: 451 Research / S&P Global Datacenter Services Outlook (Sep 2025); Pew Research analysis of EPRI 2024.
Papago
INDENG 290 Energy Analytics
05 / 16

## Slide 6
GRID STRESS · CASE 1
PJM capacity prices have risen ~10× in two years
Chart: Capacity clearing price ($/MW-day)
| 2022/23 | 2023/24 | 2024/25 | 2025/26 | 2026/27 | 2027/28
$/MW-day | 50 | 34.13 | 28.92 | 269.92 | 329.17 | 333.44
+833%
Single-year increase, 2024/25 → 2025/26 auction (PJM news release).
$9.4B
Extra cost passed to PJM ratepayers in 2025/26 — 63% attributable to data centers (Independent Market Monitor).
$70/mo
NRDC estimate of average PJM household bill increase by 2028 if cap removed.
Both 2026/27 and 2027/28 auctions cleared at the FERC-approved cap. PJM cleared 6.6 GW below its 20% reserve-margin target.
Source: PJM Base Residual Auction releases; IEEFA July 2025; NRDC October 2025.
Papago
INDENG 290 Energy Analytics
06 / 16

## Slide 7
GRID STRESS · CASE 2
ERCOT's large-load queue nearly quadrupled in a year
Chart: GW in interconnection queue
| Dec '24 | Jun '25 | Nov '25 | Jan '26
Total large-load queue | 63 | 110 | 226 | 233
Of which: data centers | 34.7 | 71.5 | 174 | 179.4
WHAT THIS MEANS
77%
of the queue is data centers.
367 GW
ERCOT preliminary 2032 peak — over 4× today's record.
23 GW
of new generation added 2024–25. The queue dwarfs supply.
ERCOT itself flagged the 2026 forecast as likely an over-estimate — "phantom load" from speculative interconnection requests is a known data-quality problem.
Source: ERCOT Long-Term Load Forecast filings (2024–2026); Latitude Media Feb 2026; Texas Scorecard Apr 2026.
Papago
INDENG 290 Energy Analytics
07 / 16

## Slide 8
ELEMENT 6 · METHODOLOGY
Three-stage approach: describe, estimate, project
STAGE 1
Descriptive analysis
Map data-center capacity by state, ISO/RTO, and zone.
Compare regions with heavy DC presence (VA, TX) to controls.
Establish stylized facts the model must explain.
Data: 451 Research, EPRI, EIA Form 861.
OUTPUT
Stylized facts
Slides 4–5
STAGE 2
Econometric estimation
Pooled OLS with state fixed effects.
Demand = α_state + β·DC_GW + γ·CDD + δ·HDD + ζ·Industrial + ε
Controls isolate the data-center effect from weather and macro activity.
Data: Constructed monthly panel, 3 states × 96 months.
OUTPUT
Causal coefficients
Slide 10
STAGE 3
Scenario projection
Three 2024–2030 scenarios: BAU, Green AI, Efficiency Breakthrough.
Each scenario adjusts demand AND fuel mix; emissions computed bottom-up.
Cumulative CO₂ compared against the BAU baseline.
Data: IEA Energy & AI, Uptime Institute, Epoch AI chip-efficiency series.
OUTPUT
2030 scenarios
Slides 11–12
Papago
INDENG 290 Energy Analytics
08 / 16

## Slide 9
ELEMENT 5a · PRELIMINARY FINDINGS — STAGE 1
Three stylized facts the data overwhelmingly support
01
Data-center demand is geographically concentrated, not diffuse.
Five states (VA, TX, OR, CA, GA) hold ~65% of U.S. capacity. VA and TX alone added ~5 GW in 2024–25.
02
Where concentration is high, capacity markets are stressed.
PJM's Dominion zone (northern Virginia) and ERCOT large-load nodes show 10× capacity-price moves and 4× queue growth respectively.
03
Cost is shifting onto residential ratepayers — for now.
Avg. PJM household bill +$18/month in W. Maryland; +$21/month for DC Pepco customers; ~$70/month estimate by 2028 absent intervention.
These facts are firm. They are documented in primary sources (PJM, ERCOT, EIA) and corroborated by independent analysis (NRDC, IEEFA, Pew).
Papago
INDENG 290 Energy Analytics
09 / 16

## Slide 10
ELEMENT 5b · PRELIMINARY FINDINGS — STAGE 2
Each new GW adds ~7.7 TWh/year to state demand
Pooled OLS, state fixed effects · N = 288 · R² = 0.926
Variable | Coefficient | Std. Error | t-stat
Data-center capacity (GW) | 0.639 | 0.024 | 26.8
Cooling degree days (CDD) | 0.272 | 0.010 | 28.2
Heating degree days (HDD) | 0.181 | 0.010 | 17.3
Industrial activity index | 8.794 | 1.585 | 5.6
DV: monthly state electricity demand (TWh). All coefficients significant at p < 0.001.
INTERPRETATION
0.64 TWh/month per GW
≈ 7.7 TWh/year — equivalent to running a 1 GW facility at ~88% load factor. Matches industry reporting for hyperscale facilities.
Wholesale-price model (R² = 0.52) shows ~$0.82/MWh increase per added GW on a linear basis — non-linearly larger in the most concentrated zones.
STATUS · PRELIMINARY
Will be re-estimated on EIA actuals once 2024 Form 861 panel is complete.
Papago
INDENG 290 Energy Analytics
10 / 16

## Slide 11
STAGE 3 · SCENARIO DESIGN
Three plausible 2024–2030 trajectories
BUSINESS-AS-USUAL
Continued rapid AI expansion
525 TWh
2030 demand
LBNL high-mid trajectory (+144% vs 2024).
Fuel mix only modestly cleaner: gas falls 41% → 38%.
Coal phase-out continues (15% → 7%).
GREEN AI TRANSITION
Strong renewable adoption by hyperscalers
525 TWh
2030 demand (same)
Demand path identical to BAU.
Renewables 24% → 55%; gas drops to 20%.
24/7 carbon-free PPAs become the dominant procurement model.
EFFICIENCY BREAKTHROUGH
Major chip + cooling efficiency gains
370 TWh
2030 demand
Chip efficiency holds 40%/yr trajectory (Epoch AI).
Industry-avg PUE drops from 1.56 → 1.30.
BAU mix retained (no clean-energy assumption).
All three scenarios use the same 2024 starting point (215 TWh). They differ in demand path, fuel mix, or both. Emissions are computed bottom-up.
Papago
INDENG 290 Energy Analytics
11 / 16

## Slide 12
STAGE 3 · SCENARIO OUTCOMES
Each lever cuts ~20% — but neither alone is enough
Chart: Demand path
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
BAU & Green AI Transition | 215 | 252 | 295 | 345 | 405 | 475 | 525
Efficiency Breakthrough | 215 | 240 | 270 | 300 | 330 | 350 | 370
Chart: Cumulative emissions
| BAU | Green AI | Efficiency
Cumulative MtCO₂ | 646 | 504 | 534
TENTATIVE FINDING
Each lever alone cuts ~17–22% of cumulative emissions vs BAU. Hitting climate targets requires both — and even then, total emissions stay far above a 2024 baseline.
Papago
INDENG 290 Energy Analytics
12 / 16

## Slide 13
EFFICIENCY LEVERS
Why we're cautious about the "efficiency will save us" story
Chart: Industry-average PUE plateaued near 1.56
| 2007 | 2011 | 2014 | 2018 | 2020 | 2022 | 2024 | 2025
Industry average | 2.5 | 1.98 | 1.7 | 1.58 | 1.59 | 1.55 | 1.56 | 1.56
Google fleet-wide | 1.16 | 1.12 | 1.11 | 1.1 | 1.1 | 1.09 | 1.09
Chart: Chip gains are real — but Jevons effect dominates
| 2018 | 2020 | 2022 | 2024 | 2026 | 2028 | 2030
Chip efficiency (FLOPs/W, indexed) | 1 | 2 | 3.8 | 7.5 | 14.8 | 28.9 | 56.7
Total DC demand (TWh, indexed) | 1 | 1.18 | 1.71 | 2.83 | 3.95 | 5.39 | 6.91
Chip efficiency improves ~40%/yr (Epoch AI) — yet aggregate demand still rises sharply because models, parameter counts, and inference volumes scale faster than per-FLOP efficiency. PUE has plateaued for the industry average since 2018; only hyperscalers approach 1.1.
Papago
INDENG 290 Energy Analytics
13 / 16

## Slide 14
ELEMENT 5b · CURRENT CONCLUSIONS
Where we land — for now
01
FIRM
AI-driven data centers are already reshaping regional grids.
PJM Dominion zone and ERCOT are not future scenarios — they are the present. Capacity prices, queue volumes, and bill increases are documented.
02
FIRM
Costs are being socialized; benefits are concentrated.
Hyperscalers capture the AI productivity surplus while ratepayers absorb capacity-market and transmission upgrades. This is politically unsustainable.
03
TENTATIVE
Efficiency alone will not bend the curve; clean-energy alone will not either.
Each lever cuts ~20% of cumulative emissions vs BAU. Hitting climate goals requires both, plus aggressive demand response and grid-flexibility programs.
04
TENTATIVE
Forecasts are highly speculative — caution is warranted.
ERCOT's own grid operator flags its 367 GW peak forecast as inflated by phantom load. LBNL's 2030 range spans 200 TWh — almost the entire 2023 total.
Papago
INDENG 290 Energy Analytics
14 / 16

## Slide 15
ELEMENT 6b · METHODOLOGICAL CHALLENGES
Three challenges — and how we're handling them
i
Limited data transparency
Problem. Hyperscalers don't disclose facility-level kWh; AI compute is not separately tracked in any utility forecast.
Approach. Triangulate from GPU shipments (NVIDIA disclosures), cloud revenue, and PUE benchmarks. Use 451 Research's facility-level capacity series as the primary spatial unit.
ii
Separating AI from general cloud growth
Problem. Both grew rapidly post-2020. A single "data center" label conflates ChatGPT-class workloads with email and storage.
Approach. Apply a difference-in-differences design: compare counties with announced AI-specific campuses (xAI Memphis, Stargate sites) to matched cloud-only counties.
iii
Establishing causality, not just correlation
Problem. Data-center growth is correlated with overall economic growth and warming summers — both drive electricity demand.
Approach. Control for CDD/HDD and a state industrial-activity index in the panel. Regression coefficient on DC capacity matches engineering bottom-up estimates (≈ 0.88 capacity factor).
Papago
INDENG 290 Energy Analytics
15 / 16

## Slide 16
ELEMENT 7 · REMAINING WORK
What's left between now and May 11
PLANNED BEFORE MAY 11
01
Re-estimate panel regression on EIA Form 861 actuals (2018–2024) once 2024 final release lands.
02
Add a fourth state (Oregon — ranked #3 in DC load) to the panel for a robustness check.
03
Run a placebo regression on counties without data-center clusters; coefficient should be near zero.
04
Sensitivity analysis on the BAU trajectory: high vs low LBNL bands to bound cumulative emissions.
05
Build a simple grid-flexibility module showing how 10% demand response on data centers shifts peak load.
THE ONE ANALYSIS WE WISH WE COULD RUN
An hourly co-simulation of AI workload shifting against renewable supply.
Why it matters.
If AI training jobs can be deferred to renewable-rich hours, the same kWh has a far lower emissions footprint. This would let us bound the upside of demand response — currently the most uncertain lever in the literature.
Why we can't.
Requires hourly load + LMP + renewable generation data across PJM, ERCOT, and CAISO, plus workload-level training schedules — none of which are publicly available at the granularity needed in the time we have.
Papago
INDENG 290 Energy Analytics
16 / 16